## Slide 1: Third Long Examination
CMSC 130
1st Semester, 2015 - 2016

## Slide 2: General Instructions
Put all circuits in a single Logisim circuit board.
Put all other answers in a PDF.
Put the CIRC and PDF file in an archive named 130_surname_le3.(any archive format)
UPLOAD (do not send) the archive on or before 1 pm tomorrow.

## Slide 3: Item #1
One way of designing a Gray code counter is by doing the following when the clock triggers the register:
  Taking the states of the register (flip flops) as input
  Converting the input to standard binary
  Adding 1 to the converted input
  Converting the added input back to Gray code
  Storing the derived Gray code to the register
Design a circuit with a 5-bit register that simulates this.
Notes: You may use either rising or falling edge as trigger

## Slide 4: Item #2
Derive the state tables and equations given the state diagram; also, design a sequential circuit that generates the diagram above.
001
100
011
010
000
1/1
0/0
1/0
0/0
1/1
0/0
1/1
0/0
0/0
1/1

## Slide 5: Item #3
Draw a PROM, PAL, and PLA diagrams for the following:
Other things to note when designing the diagrams:
  Identify the minimum possible width for the AND-OR gate array. The width should be the same for all AND-OR arrays of the PAL diagram.
  Identify the minimum number of AND gates for the PLA.